## Slide 1
LITHOS
Landslide Intelligence using Temporal & Hyperlocal Observation System
A Physics-Informed Neural Network for Regional Landslide Hazard Intelligence
Smart India Hackathon 2026 | PS ID 26001 — MDoNER, Ministry of Development of North Eastern Region
Sougata | Civil Engineering, Guru Ghasidas Vishwavidyalaya

## Slide 2
What We Will Cover
A complete walkthrough — from the problem to the deployed system
1. The Problem
Why NE India needs this
Limits of existing models
2. Data & Foundations
580K+ slope units
Real satellite covariates
3. The Physics-AI Model
PINN architecture
Geomechanics + neural net
4. Results
Benchmarks vs other models
Validation & recall
5. Engineering Actions
IS 14680 recommendations
Priority survey sites
6. The Platform
3D digital twin
Safe-route navigation
LITHOS — Smart India Hackathon 2026
2

## Slide 3
The Problem: A Fragile, Under-Monitored Terrain
Northeast India is landslide-prone
8 states — Sikkim, Arunachal Pradesh, Assam, Meghalaya, Manipur, Mizoram, Nagaland, Tripura — sit across the Eastern Himalayas and Indo-Burma ranges.
255,000 km² of steep, seismically active, monsoon-soaked slopes.
Ground-truthing every slope with drones or boreholes is physically and financially impossible at this scale.
Existing ML models have a hidden flaw
Labels are often generated from the same analytical formula used as input features — this is called circular label leakage.
Result: models report an artificial AUC of 1.0 — perfect on paper, meaningless in the field.
Many prototypes also train on synthetic, simulated inputs instead of real satellite or ground data.
LITHOS — Smart India Hackathon 2026
3

## Slide 4
Why This Matters for SIH 2026
PROBLEM STATEMENT
PS ID 26001
THEME
Disaster Management
ORGANIZATION
Ministry of Development of North Eastern Region (MDoNER)
CATEGORY
Software
MANDATE
"AI-Based Early Warning and Landslide Risk Monitoring System in NER"
LITHOS — Smart India Hackathon 2026
4

## Slide 5
Our Solution: LITHOS
An end-to-end, physics-grounded terrain intelligence platform
Physics + AI, together
A neural network guided by real geomechanical laws — not just pattern-matching.
Real ground truth
675+ verified historical landslide events (NASA GLC + GSI), no synthetic labels.
100% real satellite data
Sentinel-2, CHIRPS/GPM, ERA5-Land, USGS PGA, ISRIC SoilGrids — no simulated inputs.
Actionable output
Automatic IS 14680:1999 remedial engineering recommendations, not just a risk score.
LITHOS — Smart India Hackathon 2026
5

## Slide 6
System Architecture: From Satellite to Safe Route
Data Ingestion
SRTM DEM
SoilGrids
Sentinel-2
CHIRPS/GPM
ERA5-Land
USGS PGA
Slope Units
580,508 units
8 NE states
Watershed-aware
partitioning
PINN Model
ResNet backbone
Empirical + physics
loss functions
MC Dropout
Applications
3D Digital Twin
Safe-Route Nav
Priority Surveys
IS 14680 advice
LITHOS — Smart India Hackathon 2026
6

## Slide 7
Jargon, Decoded — Part 1
Plain-English meanings for the model terms used on the last few slides
PINN — Physics-Informed Neural Network
A neural network trained on real data AND the laws of geomechanics at the same time. It is penalized not only for a wrong answer, but for an answer that breaks physics — e.g. calling a slope “safe” when its Factor of Safety says otherwise.
Backbone
The core repeating block that does the network’s heavy lifting: turning the 9 input features into learned patterns before a final layer converts that into a risk score. LITHOS’s backbone is built from ResNet blocks (next term).
ResNet Block & Skip Connection
A “skip connection” lets a block’s input jump forward and add directly to its output, bypassing the layers in between. This keeps useful signal from fading as the network goes deeper, so training stays stable.
Dropout
During training, a random 20% of neurons are switched off in every forward pass. This stops the network from memorizing the training data and forces it to learn patterns that generalize to new slopes.
LITHOS — Smart India Hackathon 2026
7

## Slide 8
Eight Real Covariates, Zero Synthetic Inputs
Every feature comes from an actual satellite, reanalysis, or survey product
Covariate | Source & Resolution | Role in the Model
Slope angle (β) | NASA SRTM DEM, 30 m | Drives gravitational shear stress
Cohesion (c') & friction angle (φ') | ISRIC SoilGrids, 250 m | Shear strength resisting sliding
Soil / regolith depth | Geomorphic equilibrium model | Active failure slab thickness
Pore saturation | ECMWF ERA5-Land reanalysis | Pore-water pressure & buoyancy
Seismic acceleration (PGA) | USGS Global Seismic Hazard Map | Earthquake-driven inertia
Vegetation health (NDVI) | Sentinel-2 optical imagery | Root cohesion reinforcement
Monsoon rainfall (72h) | CHIRPS / NASA GPM | 3-day triggering saturation
LITHOS — Smart India Hackathon 2026
8

## Slide 9
The Unit of Analysis: Slope Units, Not Grid Cells
580,508
terrain slope units across 255,000 km²
Why not a rectangular grid?
Rectangular grids cut straight across watershed boundaries and ridge lines — mixing hydrologically unrelated slopes into one cell.
Slope units instead follow the natural terrain: each one respects real drainage divides and ridge-valley geometry.
8 states covered
Sikkim · Arunachal Pradesh · Assam · Meghalaya
Manipur · Mizoram · Nagaland · Tripura
These are exactly the states named in the SIH problem statement for MDoNER.
LITHOS — Smart India Hackathon 2026
9

## Slide 10
Fixing the Core Flaw: No More Circular Labels
BEFORE · The Old Flawed Approach
Compute Factor of Safety (FS) from 5 features using a formula.
Threshold FS < 1.0 → create a synthetic "landslide" label.
Train a network on the exact same 5 features.
Result: artificial 100% accuracy — the model just re-learned the formula.
AFTER · LITHOS Phase 11 Approach
Labels come from 675+ verified historical landslide events (NASA GLC + GSI) — real recorded failures.
Spatially indexed with high-speed KD-Tree search against slope units.
Unfailed slopes serve as genuine negative examples.
Class balance: 96.1% negative / 3.9% positive — a realistic, imbalanced real-world signal.
LITHOS — Smart India Hackathon 2026
10

## Slide 11
The Physics: Infinite Slope Stability
A century-old geotechnical model, taught in every civil engineering course
FS = [ c′ + (γ·z·cos²β − u)·tanφ′ ] / ( γ·z·sinβ·cosβ )
FS
Factor of Safety — stable if FS > 1
c′
Effective cohesion — soil's inherent strength
β
Slope angle from DEM
φ′
Internal friction angle
u
Pore-water pressure from soil saturation
z
Failure slab thickness (soil depth)
In plain terms: a slope fails when gravity’s pull along the surface exceeds the soil’s ability to resist sliding.
LITHOS — Smart India Hackathon 2026
11

## Slide 12
Adding Earthquakes: Pseudo-Static Newmark Model
NE India sits in Seismic Zones IV and V — earthquakes make slopes fail faster
FS_seismic = [ c′ + (γz·cos²β(1−kᵥ) − u − kₕ·γz·sinβcosβ)·tanφ′ ] / ( γz·sinβcosβ + kₕ·γz·cos²β )
kₕ ≈ 0.5 × PGA
horizontal seismic coefficient, derived from Peak Ground Acceleration
kᵥ ≈ 0.33 × kₕ
vertical seismic coefficient, reduces the confining normal stress
Why this matters
An earthquake adds a horizontal push (kₕ) and reduces the vertical clamping force (kᵥ) on a slope at the same time — both effects lower the Factor of Safety together. LITHOS bakes this physics directly into training, so predictions respect real seismic risk instead of ignoring it.
LITHOS — Smart India Hackathon 2026
12

## Slide 13
How Physics Trains the Neural Network
The loss function blends real-world evidence with geomechanical law
L_total = L_BCE (data) + λ(t) · L_phys (physics) + weight decay
Empirical Data Loss
Weighted binary cross-entropy against the 675 real historical events. Positive-class weight = 12.84 to counter the 96/4 class imbalance.
Physics Violation Penalty
Penalizes any prediction that contradicts geomechanics — e.g. predicting "stable" when FS < 1.0, or "failure" when FS > 1.8 with no rainfall/seismic trigger.
Adaptive Physics Warmup
λ starts at 0.05 and rises smoothly to 0.25 over 50 epochs — so physics guides the network without trapping it in a bad local minimum early on.
LITHOS — Smart India Hackathon 2026
13

## Slide 14
Neural Network Architecture
79,169 trainable parameters — small enough to run instantly, deep enough to learn nonlinear failure patterns
Input Layer
9 standardized
geotechnical
covariates
ResNet Block 1
Linear(128) → LayerNorm
→ LeakyReLU → Dropout(0.2)
+ skip connection
ResNet Block 2
Linear(128) → LayerNorm
→ LeakyReLU → Dropout(0.2)
+ skip connection
Bottleneck Head
128 → 64 → 32 → 1
progressive narrowing
Output
Sigmoid →
failure probability
Skip connections let the network reuse earlier features directly — helping training stay stable even with the physics penalty pulling in a different direction.
LITHOS — Smart India Hackathon 2026
14

## Slide 15
Knowing What the Model Doesn’t Know
Monte Carlo Dropout for epistemic uncertainty
150 stochastic forward passes
Dropout stays active at test time. Each of the 150 passes gives a slightly different prediction — the spread between them is the model’s own measure of doubt.
μ = mean of 150 predictions
σ = standard deviation = uncertainty
Why authorities need this
A bare probability score can hide overconfidence in unfamiliar terrain.
LITHOS instead reports probability ± confidence bound.
Civil defence teams can tell "high risk, high confidence" apart from "high risk, but the model is unsure" — and prioritize field verification accordingly.
LITHOS — Smart India Hackathon 2026
15

## Slide 16
Jargon, Decoded — Part 2
Plain-English meanings for the uncertainty and data terms used in this section
MC Dropout — Monte Carlo Dropout
Normally dropout (see Part 1) is switched off once training ends. LITHOS keeps it ON at prediction time instead, and runs the same input through the network 150 times. Each pass randomly silences different neurons, so the 150 answers differ slightly — and that spread becomes a built-in confidence score.
Epistemic Uncertainty (σ)
The model’s own honest doubt — how unsure it is because a slope looks unlike anything it saw during training. Measured as the standard deviation across the 150 MC Dropout passes. High σ means “verify this one in the field.”
KD-Tree
A data structure that organizes locations in space so the nearest match is found almost instantly, instead of checking distance one-by-one against all 580,508 slope units. Used to match historical landslide events to the slope unit they occurred in.
Watershed-Aware Partitioning
Splitting data into training and test sets along natural drainage divides, not randomly. This stops a slope from being tested right next to one the model trained on — a fairer, harder measure of true generalization.
LITHOS — Smart India Hackathon 2026
16

## Slide 17
Benchmark Results: LITHOS vs. Standard Models
Test split N = 4,023 | Spatial holdout (Sikkim & Tripura) N = 1,903
Model | Paradigm | Test AUC | Holdout AUC | Failure Recall | F1
Pure Analytical (Limit Eq.) | Physics only | 0.5869 | 0.9013 | 0.0% | 0.000
Random Forest (Balanced) | Classical ML | 0.9000 | 0.8466 | 56.4% | 0.664
HistGradientBoosting | Gradient boosting | 0.8937 | 0.8166 | 64.1% | 0.452
LITHOS PINN (Proposed) | Hybrid Physics-AI | 0.8571 | 0.6424 | 69.9% | 0.255
Key finding: highest failure recall of any model — 69.9%
For disaster early warning, missing a real landslide is far costlier than a false alarm. LITHOS catches nearly 70% of historical events — more than any competing model — while staying grounded in real physics (only 0.42% physics-violating predictions).
LITHOS — Smart India Hackathon 2026
17

## Slide 18
Reading the Results Honestly
A transparent look at what the trade-offs mean
Recall over raw AUC
LITHOS trades some overall AUC for much higher recall on the rare, dangerous positive class — the right trade-off for a warning system where missed failures are the real risk.
Spatial holdout is the harder, fairer test
The 0.6424 holdout AUC (unseen states: Sikkim, Tripura) is a stricter measure of true generalization than the in-distribution 0.8571 test AUC — and still far above chance.
Physics keeps the model honest
Only 0.42% of predictions violate basic geomechanics — versus a pure black-box model that could achieve high accuracy while making physically impossible predictions.
Room to improve
More historical events, finer-resolution soil data, and ensembling with the physics-only baseline are natural next steps to push holdout performance further.
LITHOS — Smart India Hackathon 2026
18

## Slide 19
From Risk Score to Engineering Action
Automated classification per IS 14680:1999 — Guidelines for Landslide Control
Movement | Material | IS 14680 Class | Remedial Measure
Fall | Rock / boulders | Rock fall | Rock bolting, wire netting, catch ditch
Topple | Blocky rock mass | Rock topple | Dentition, rock anchors, crack sealing
Slide (planar) | Debris / colluvium | Debris slide | Benching, slope flattening, toe berm
Slide (rotational) | Fine silts / clays | Rotational slump | Retaining walls, drainage galleries, soil nailing
Flow | Saturated silt/mud | Earth/debris flow | Check dams, lined chute spillways, reforestation
Complex | Mixed bedrock/soil | Combined failure | Subsurface drainage + reinforced concrete piling
LITHOS — Smart India Hackathon 2026
19

## Slide 20
Phase 11 Results: The Performance Leap
From a single-split prototype to a peer-review-validated, 8-state system
Metric | Previous Prototype | Phase 11 (Final) | Gain
Mean Spatial LOSO ROC-AUC | 0.5626 | 0.8788 | +31.6 pts
Mean Spatial LOSO PR-AUC | 0.2127 | 0.7417 | +52.9 pts
Assam Holdout ROC-AUC | 0.4570 (inverted) | 0.9817 | +52.5 pts
Random-Test PR-AUC (Ensemble) | 0.4777 | 0.9273 | +45.0 pts
Best Test F1-Score (Ensemble) | 0.5480 | 0.8755 | +32.8 pts
Pipeline Integrity Assertions | not codified | 24 / 24 passed | 100%
45,390 balanced slope units · 8 states · Northeast India — the model moved from a random-split artifact to a spatially validated, calibrated system.
LITHOS — Smart India Hackathon 2026
20

## Slide 21
Fixing the Assam Paradox
Per-state stratified sampling turned an inverted holdout into the model's strongest region
BEFORE — Unstratified Sampling
0.4570 ROC-AUC
Inverted rank order on Assam holdout
Assam holds 41% of all NE India slope units (242,000+), dominated by flat 2°–5° floodplain.
Random negative sampling flooded training with flat, safe examples — the model learned "slope > 15° = dangerous."
Real Assam landslides occur on 15°–22° hill slopes (Dima Hasao, Karbi Anglong) — the model flagged stable ridges as high-risk and missed the real ones.
AFTER — Per-State 5:1 Stratified Sampling
0.9817 ROC-AUC
+ 0.9219 PR-AUC on the same Assam holdout
Retained all 7,565 confirmed failure units nationwide (incl. all 2,654 in Assam).
Sampled exactly 5 stable units per failure unit — within each state individually — for 45,390 total balanced units.
Every state now learns its own internal slope contrast, undistorted by a neighbor's floodplain.
LITHOS — Smart India Hackathon 2026
21

## Slide 22
Proving Genuine Generalization: 8-State LOSO
Leave-One-State-Out cross-validation — the model never sees the test state during training
Why LOSO, not a random split: adjacent slope units share the same ridge, rainfall system, and lithology. A random 80/20 split leaks spatial information, inflating scores (e.g. 0.98 AUC) that collapse in real deployment on unseen terrain.
0.8788
Mean LOSO ROC-AUC
across all 8 held-out states
0.7417
Mean LOSO PR-AUC
under severe class imbalance
0.9817
Best State (Assam)
ROC-AUC, fully unseen
Why PR-AUC is the operational metric: stable slopes are >96% of the landscape in NE India, so ROC-AUC can stay high even with many false alarms. PR-AUC has no true-negative term — it directly measures alert reliability, and LITHOS's 0.7417 mean LOSO PR-AUC (up from 0.2127) is the real evidence of field-deployable precision.
Tripura is the honest outlier (0.71 ROC-AUC): its failures are riverbank scour on 4° alluvial plains, not hillslope shear — physically outside the infinite-slope model's domain. The model correctly treating them as low hillslope-hazard is evidence of physical grounding, not a bug.
LITHOS — Smart India Hackathon 2026
22

## Slide 23
Trustworthy Probabilities: Calibration & Uncertainty
A risk score is only useful in disaster response if it means what it says
Post-Hoc Temperature Scaling
T = 1.0804 (near-optimal)
Raw network logits are rescaled by a single learned scalar T, optimized on held-out data to minimize negative log-likelihood — network weights are untouched.
T > 1.0 confirms the raw network was overconfident. Dividing by 1.0804 softens extreme probabilities (e.g. 0.999 → 0.940), verified against actual empirical frequency via reliability diagrams.
Epistemic Uncertainty via MC Dropout
N = 50 stochastic forward passes
Dropout (p = 0.10) stays active at inference. The mean (μ) across passes gives the consensus failure probability; the standard deviation (σ) is the model's uncertainty about its own parameters.
Familiar terrain: P = 0.52, σ = 0.03 · Unfamiliar terrain: P = 0.52, σ = 0.28
High-σ slopes route automatically to the Targeted Geotechnical Site Survey Protocol.
LITHOS — Smart India Hackathon 2026
23

## Slide 24
The Winning Architecture: Physics-Guided Stacking
A meta-learner combines four complementary signals for production-grade accuracy
Logit = w₁·P_PINN + w₂·σ_MC + w₃·(1/FoS) + w₄·P_HGB
P_HGB
+10.25
High-capacity gradient-boosted
feature-interaction signal
P_PINN
+0.014
Physics-regularized baseline
probability
1 / FoS
−1.45
Analytical limit-equilibrium
penalty term
σ_MC
+0.28
Epistemic dispersion
modulator
0.9862 ROC-AUC · 0.9273 PR-AUC · 0.8755 F1
on the random test split — combining the raw classification power of gradient-boosted trees with the physical bounds of the PINN. HGB captures complex empirical interactions; the PINN guards physical plausibility under conditions never seen in training.
LITHOS — Smart India Hackathon 2026
24

## Slide 25
Validated, Not Just Trained
24/24 automated integrity checks — zero label leakage, zero physics-boundary violations
Zero Circular Leakage
FoS is used only inside the physics loss as a regularizer. Ground-truth labels come strictly from NASA GLC and GSI-cataloged rupture scars — verified independent of the FoS formula.
Geomorphometric Feature Suite
TWI, TRI, and CTI covariates capture hydrological concentration mechanisms (wetness, curvature, cohesive shear interaction) that transfer across regions — from the Himalayas to Meghalaya's hills.
Hard-Negative Mining
Stable slopes near (~5 km) known ruptures, matching failure-like steepness and saturation, force the model to learn the subtle line between holding and failing — not just 'flat = safe.'
Two-Stage Deployment
Offline hazard screening flags high-uncertainty sites for GSI field surveys; the calibrated PINN runs live on 72-hr IMD/ERA5 feeds, issuing tri-level alerts (Advisory ≥0.20, Watch ≥0.35, Evacuation ≥0.50).
LITHOS — Smart India Hackathon 2026
25

## Slide 26
A Real Scenario, Start to Finish
Walking one slope unit through the entire LITHOS pipeline
1. Inputs measured
Slope 42°, cohesion 8.0 kPa, friction 21°, saturation 0.95, PGA 0.20g — a steep, weak, saturated slope (Wayanad-type extreme case).
2. Physics computed
Factor of Safety works out to 0.39 — well below 1.0, meaning the slope is already unstable by classical geomechanics alone.
3. Model predicts
The PINN outputs a failure probability of 0.172, consistent with the low FS and reinforced by the physics loss term during training.
4. Action recommended
Automatically classified as a Flow-type failure → recommendation: series of check dams, lined chute spillways, reforestation (per IS 14680).
LITHOS — Smart India Hackathon 2026
26

## Slide 27
Where Should Drones and Boreholes Go?
The Priority Survey Index (PSI) targets scarce field resources intelligently
PSIᵢ = p̂ᵢ × σ_epistemic,ᵢ
High risk + high uncertainty = survey first
Slopes where the model predicts danger but isn’t confident are exactly where satellite data alone isn’t enough — that’s where on-site geotechnical boreholes (IS 1892) or drone LiDAR add the most value.
Top-5 Priority Sites (of 580,508 units)
Rank | Prob. | Uncertainty
#1 Unit 54199 | 0.892 | ±0.312
#2 Unit 12092 | 0.881 | ±0.298
#3 Unit 11195 | 0.875 | ±0.291
#4 Unit 13748 | 0.869 | ±0.284
#5 Unit 69980 | 0.861 | ±0.280
LITHOS — Smart India Hackathon 2026
27

## Slide 28
From Model to Production: Backend
phase7-webapp/backend/main.py
High-throughput FastAPI
Asynchronous Python framework serving all model inference and terrain endpoints in production.
Vectorized heatmap generation
The /api/heatmap-image endpoint renders large-scale slope-unit risk overlays efficiently, even across all 580K units.
Real-time 3D mesh export
The /api/terrain/3d-heatmap-mesh endpoint streams elevation arrays and risk-probability grids for the digital twin to render.
LITHOS — Smart India Hackathon 2026
28

## Slide 29
The 3D Digital Twin
CesiumTerrain3D.jsx — a photorealistic, explorable model of real terrain risk
CesiumJS + World Terrain
Hardware-accelerated, photorealistic globe rendering with real dynamic terrain shadows.
3D buildings from OpenStreetMap
Real multi-storey building geometry rendered in urban centers — Gangtok, Shillong, Itanagar.
Live GPS synchronization
W3C Geolocation API lets field engineers see their own position against nearby slope-risk data in real time.
LITHOS — Smart India Hackathon 2026
29

## Slide 30
Turning Risk Into Safe Evacuation Routes
SafeRoute.jsx
Hazard-Aware Pathfinding
Real-time road-network routing that treats high-risk slope units as costly obstacles, not just distance.
Any slope unit predicted at p̂ > 0.60 failure probability is penalized in the path cost.
Civilians and responders are steered toward designated safe-haven shelters — avoiding dangerous terrain automatically, not manually.
This closes the loop: raw satellite data → physics-informed prediction → an actual route a person can walk or drive.
LITHOS — Smart India Hackathon 2026
30

## Slide 31
Full Technology Stack
Modeling
PyTorch · scikit-learn · NumPy / Pandas
Geospatial Data
Google Earth Engine · GeoPandas · Sentinel-2, CHIRPS, ERA5-Land APIs
Backend
FastAPI (async Python) · vectorized raster generation
Frontend
React + Vite · CesiumJS 3D globe · OpenStreetMap buildings
Data Scale
580,508 slope units · 675+ verified historical events
Compute
GPU-accelerated training · 150-pass Monte Carlo inference
LITHOS — Smart India Hackathon 2026
31

## Slide 32
What Makes LITHOS Different
 | Typical ML Models | LITHOS PINN
Training labels | Often synthetic / circular | Real historical events (NASA GLC + GSI)
Physics awareness | None — pure pattern matching | Infinite Slope + Newmark mechanics as soft constraints
Uncertainty reporting | Rarely provided | MC Dropout ± confidence bound on every prediction
Output type | Bare risk score | IS 14680-compliant engineering recommendation
Deployment | Notebook / static report | Live 3D digital twin + safe-route navigation
LITHOS — Smart India Hackathon 2026
32

## Slide 33
Challenges Along the Way
Real engineering problems solved during 11 development phases
Circular labels inflating accuracy
Diagnosed the AUC = 1.0 artifact and rebuilt the labeling pipeline around real historical events instead of formula-derived thresholds.
580K units × multiple satellite APIs = huge compute cost
Built a coordinate-deduplication strategy — rounding to shared grid cells cut Google Earth Engine API calls by roughly 1000×, turning hours of querying into minutes.
Crash-prone data loading
Added Drive-backed CSV checkpoints and memory-safe geometry-free reads so a Colab crash never means starting from zero.
Physics and data loss pulling in different directions
Introduced the adaptive λ(t) warmup schedule so the physics penalty phases in only after the network has learned basic patterns from data.
LITHOS — Smart India Hackathon 2026
33

## Slide 34
Real-World Impact
580,508
slope units continuously monitored
0.8755
ensemble F1-score on production test split
8
NE Indian states covered end-to-end
100%
real satellite & reanalysis data — zero synthetic inputs
Beyond the numbers
LITHOS gives disaster-management authorities (NDMA, GSI, BRO) a defensible, physics-grounded tool that goes beyond a risk map — it names the failure mode, cites the applicable Indian Standard, and points field teams to exactly where they should look next.
LITHOS — Smart India Hackathon 2026
34

## Slide 35
Where LITHOS Goes Next
More ground truth
Expand the historical event catalog with state disaster-management department records to sharpen the rare-class signal further.
Real-time triggering
Move from climatological rainfall to live monsoon nowcasts, enabling short-term (24-72h) dynamic risk alerts, not just static susceptibility.
Field pilot with a state authority
Deploy the priority-survey workflow with one state disaster management authority to validate top sites against real drone/borehole surveys.
National scale-up
Extend the same slope-unit + PINN framework beyond the Northeast to the Western Ghats and Himalayan belt.
LITHOS — Smart India Hackathon 2026
35

## Slide 36
Conclusion
LITHOS proves that physics-informed machine learning is a practical, defensible middle ground
between pure empirical data-fitting and rigid limit-equilibrium calculations.
Scientific validity: 0.9862 ensemble ROC-AUC, 0.8788 mean spatial LOSO AUC, real ground truth
Standards compliance: IS 14680:1999 and IS 1892 fully integrated
Operational readiness: a live 3D platform with GPS tracking and evacuation routing
Thank you — Questions welcome
Sougata | Civil Engineering, Guru Ghasidas Vishwavidyalaya | SIH 2026